Распространенные интерфейсы  компьютеров

Interface            Format    NumbDevices     Distance          Speed          Typical Use

(maximum)      (maximum,       (maximum,

feet)          bits/sec.)

USB                   asynchr      127            16 (up to 96 ft   1.5M, 12M,     Mouse, keyboard,

serial  .                              with 5 hubs),     480M         drive, audio, printer,

other peripherals

Ethernet             serial    1024                1600                 10G                  General network

communications

IEEE-1394b      serial      64                   300                  3.2G                  Video, mass

(FireWire 800)                                                                                          storage

IEEE-488         parallel   15                       60                   8M                  Instrumentation

(GPIB)

IrDA               asynchr        2                      6                  16M          Printers, hand-held computers

serial infrared                                                           hand-held computers

I2C                 synchr                                                                               Microcontroller

Serial          40                    18                  3.4M                 communications

Microwire       synchr                                                                                Microcontroller

Serial          8                     10                    2M                   communications

MIDI               serial     2 (more with       50                   31.5k                Music, show control

current    flow-through

loop       mode)

Parallel                                                    10–30              8M                     Printers,

Printer Port  parallel       2 (8 with                                                            scanners, disk

daisy-chain                                                           driver

support)

RS-232         asynchr      2                    50-100              20k                        Modem, mouse,

(EIA/TIA-232) serial                                                    (115k with               instrumentation

some

hardware)

RS-485         asynchr     32 unit loads   4000                10M                      Data acquisition

(TIA/EIA-485) serial     (up to 256                                                            and control

devices with                                                          systems

some

hardware)

SPI                synchr      8                        10                  2.1M                    Microcontroller

Serial                                                                                     communications